## Slide 1: The prediction of Gas Isotherms by the Structures of Metal-Organic Frameworks
Group 6:
Wenqin You
Zhe Liu
04/17/2018

## Slide 2: Background: Gas Adsorption
Adsorption is one of the most essential processes in chemical engineering.

## Slide 3: Background: Metal-Organic Frameworks
MOFs are good candidates for gas adsorption:
  High surface area, porosity, and functionality
Applications for adsorptive separation:
  Energy issue: CH4 uptake
  Global warming issue: CO2 capture
  Industrial example: C2H4/C2H6 separation
  The search for the optimal MOF requires aggressive screening of a variety of MOFs

## Slide 4: Motivation of the prediction of the isotherm
Goal: Isotherm = f(structure info …) without exp. or GCMC
Experimental Measurement
Measurement takes long time
Synthesis of new MOFs : >12h
Accuracy depends on exp. conditions
Grand canonical Monte Carlo(GCMC)
Couple hours
Require accurate force field
Prediction by
machine learning
A few seconds/minutes
Rapid screening
Advice for material design

## Slide 5: Workflow for Data Cleaning and Retrieval
NIST: 6000 adsorbents
Zeolites
MOFs
124 MOFs
w/ isotherms
Other adsorbents
Training/Test Examples
124 MOFs have
matched structure info.
Activated Carbon
Remove non-MOFs, such as Zeolites and AC
Convert pressure unit and adsorption unit
1. Remove MOFs with missing structure properties
MOFs not matched
Isotherms in NIST
adsorption database
Structure information
in computational-ready experimental (CoRE)
MOFs database
Notes: Remove non-MOFs, such as Zeolites and AC
Convert pressure unit and adsorption unit
Remove MOFs with missing structure properties

## Slide 6: Workflow for CoRE MOFs Database
Define the feature vectors
  Each MOF can be represented by PLD, LCD, SA, VF and density etc.
  Metals type as numerical variables
Metal type:
  Atomic mass (ma)
  Atomic radius(ra)
  Electronegativity()
Density (ρ)
pore-limiting diameter (PLD)
largest-cavity diameter (LCD)
Volumetric Surface area (VSA)
Gravimetric Surface area (GSA)
Pore volume (PV)
Void fraction (VF)
Principle Component Analysis
  Calculate the explained variance
  Minimum # of principle components

## Slide 7: Workflow for NIST Adsorption Database
Linear Regression on Isotherms
  Curve-fit isotherm data
Isotherm Type Assignment
  Assign model based on R2 value
  Keep R2 higher than 0.95 (cutoff value)
CuBTC
CO2
276K
Langmuir: (Q0, b)
Freundlich: (K, n)
Notes: Q0Q0 is maximum monolayer coverage capacities, b is Langmuir isotherm constant
K is Freundlich isotherm constant related to adsorption capacity.

## Slide 8: Workflow for machine learning
Final Model
Classification:
Regression:
Langmuir:
Freundlich:
Results from NIST:
MOFs labeled with model, and corresponding parameters
Results from CoRE MOFs
MOFs and their structure properties after PCA
Machine
Learning
Notes: Adsorbates:
CO2
CH4
N2
H2
O2

## Slide 9: Result 1: Isotherm classification for N2
Methods | Logistic | LDA | KNN | Kernel SVC
Accuracy | 41.8% | 70.9% | 82.3% | 83.5%
Cross Validation | 24.1% | 67.0% | 82.3% | 74.7%

## Slide 10: Result 2: Regression of N2 by Linear Regression
Langmuir:
Parameters by LR | R2 | CV mean relative error
Q0 | 0.78 | 1.02
b | 0.24 | 3.02

## Slide 11: Result 2: Regression of N2 by Linear Regression
Freundlich:
Parameters by LR | R2 | CV mean relative error
K | 0.38 | 0.85
n | 0.29 | 1.22

## Slide 12: Result 3: Regression of N2 by Kernel SVR, RBF
Langmuir:
Parameters by SVR | R2 | CV mean relative error
Q0 | 0.87 | 0.53
b | 0.53 | 2.44

## Slide 13: Result 3: Regression of N2 by Kernel SVR, RBF
Freundlich:
Parameters by SVR | R2 | CV mean relative error
K | 0.75 | 1.10
n | 0.60 | 1.35

## Slide 14
Classification of isotherm models:
  Tried Logistic, LDA, KNN, SVC method to classify
  Both KNN and SVC work well. (KNN:82.3% mean accuracy, CV)
Regression of isotherm parameters for each model:
  Tried linear regression and support vector regression with RBF
  SVR works well with higher R2 and lower CV mean relative error
Analysis on Data source :
  Same MOF has different isotherm results
  Training examples are not large enough (124 matched MOFs)
Future plan:
  Adding more isotherm types during the model assignment
  Gather more matched MOFs manually to increase the training set
  Consider the chemical information of MOFs as the feature vector: use more variables to describe metals and organic linkers
Discussion and Conclusions
Notes: Assignment of adsorption models for each isotherm
Aim: predict isotherms by the structure info. of MOFs
  Input (feature vector): MOF structure information
  Output is category: classification of isotherm models
  Output is number: regression of isotherm parameters
Data source:
  NIST adsorption data is not good enough.
    Empty data points
    Negative pressure or adsorption
    Same MOF has different isotherm results.
  GCMC calculation can provide more accurate isotherm database.
  Future prediction of isotherm by ML can base on GCMC.

## Slide 15: Questions

## Slide 16: Backup: Adsorbent Structural Descriptors
Density (ρ) g/cm3
Volumetric Surface area (VSA) m2/cm3
Gravimetric Surface area (GSA) m2/g
Pore volume (PV): cm3/g
Void fraction (VF)
pore-limiting diameter (PLD): Å
largest-cavity diameter (LCD): Å
Metal type:
  Atomic mass (ma)
  Atomic radius(ra)
  Electronegativity()

## Slide 17: Backup: These authors also explored the trade-off between volumetric capacity and gravimetric capacity. The results show a concave downward relationship between volumetric and gravimetric storage capacities.